## Slide 1: 模拟与数字电路 Analog and Digital Circuits
18_数字系统设计

## Slide 2: 主要内容
数字系统结构
算术逻辑单元
寄存器传送和总线
求最大值和排序
时序乘法器
Notes: 2

## Slide 3: 数字系统结构
数字系统
  由若干逻辑功能部件构成，按一定时序控制和处理的数字电路
  从结构上划分为数据通路和控制单元两部分
数据通路(Data Path)
  数据在被处理过程中经过的路径
控制单元 (Control Unit)
  控制数据通路中数据的流动方向和次序
数据通路
数据输入
数据输出
控制单元
控制输入
控制
状态
数字系统结构框图
状态输出

## Slide 4: Design Hierarchy
switching networks
datapath
control
state registers
combinational logic
data registers
register
logic
combinational logic
digital system

## Slide 5: 算术逻辑单元
算术逻辑单元（ALU）
  s：功能选择。加、减、与、或、非、异或等运算
  a, b：两操作数。减运算-- a是被减数；非运算--操作数是a
  y：运算结果。和、差 ……
  f：标志。进位/借位 (cf)、溢出 (of)、零标志 (zf)
k
n
n
a
b
f
s
m
y
n
ALU
s | y | cf | of | zf
000 | a + b | * | * | *
001 | a - b | * | * | *
100 | a & b | 0 | 0 | *
101 | a ¦ b | 0 | 0 | *
110 | a ^ b | 0 | 0 | *
111 | ~ a | 0 | 0 | *
其他 | 0 | 0 | 0 | 1
ALU功能表
表中“*”表示根据运算结果设置相应值

## Slide 6: ALU模块化设计
s | y | cf | of | zf
000 | a+b | * | * | *
001 | a-b | * | * | *
100 | a&b | 0 | 0 | *
101 | a¦b | 0 | 0 | *
110 | a^b | 0 | 0 | *
111 | ~a | 0 | 0 | *
其他 | 0 | 0 | 0 | 1
k
n
n
a
b
f
s
m
y
n
ALU
a & b
a | b
s
~ a
a ^ b
s0
a
b
ya
+/−
fa
MUX
y
f
ALU功能表

## Slide 7: ALU模块化设计 (续)
a & b
a | b
s1s0
0
1
2
3
~ a
a ^ b
y2
s1
0
0
1
s2
0
1
s0
a
b
ya
+/−
fa
s2|s1
0
0
1
zf
y
cf, of
= 0

## Slide 8: 寄存器传送
寄存器之间传输数据
每个寄存器的数据输入处配置多路数据选择器(MUX)
每个寄存器的输出数据连接到所有MUX
灵活实现多个数据同时传送
E0
E1
E2
R0
E
R1
E
R2
E
S0
S1
S2
n
n
MUX
S
0
1
n
n
n
MUX
S
0
1
n
n
n
MUX
S
0
1
n
R0 R1
// S0=1, E0=1
// S1=0, E1=1
// S2=x, E2=0

## Slide 9: 总线
BUS：多个部件共享用于传输数据的一组导线
  每次只能传送一个数据
R0  R1
//S=1, E0=1
E0
n
R0
E
S
MUX
S
0
1
2
n
n
E1
n
R1
E
n
E2
n
R2
E
n
2
R0  R1
//C1=1, E0=1
//C0=0, C2=0
E0
E1
E2
R0
E
R1
E
R2
E
n
C0
n
n
C1
n
n
C2
n
BUS
BUS

## Slide 10: 寄存器堆
也称寄存器文件(Register File)
例如，有3个读写端口的2m个n位寄存器，其中
1个写端口
  WA：写地址
  WD：写入数据
  WE：写使能
2个读端口
  RA0、RA1：读地址
  RD0、RD1：读出数据
寄存器堆
(2m×n)
RD0
RD1
WD
WA
RA0
RA1
WE
n
n
n
m
m
m

## Slide 11: 寄存器堆 (续)
M
U
X
0
1
2
3
R0
D
E
R1
D
E
R2
D
E
R3
D
E
M
U
X
0
1
2
3
Decoder
0
1
2
3
E
A
RD0
RD1
WD
WA
RA0
RA1
WE
2
2
2
n
n
n
n
n
n
3端口4×n寄存器堆
n

## Slide 12: 寄存器堆 (续)
// m = 5, n = 32
wire [31:0] rd0, rd1;
reg [31:0] regfile [0:31];
assign rd0 = regfile [ra0],
rd1 = regfile [ra1];
always @ (posedeg clk)
if (we) regfile [wa] <= wd;
寄存器堆
(2m×n)
RD0
RD1
WD
WA
RA0
RA1
WE
n
n
n
m
m
m

## Slide 13: 示例：求最大值
x1
x0
MAX
start
x2
rstn
y
f
4
4
clk
IDLE
LOAD
CMP1
CMP2
! rstn
start
! start
思考题：有符号数如何？
CU
clk
rst
cf
s
f
start
e
2
3
s0
“-”
cf
ALU
R1
R0
R2
x0
x2
x1
y
0
1
0
1
s1
s1-0 | e2-0 | f
xx | 000 | 1
x0 | 111 | 0
01 | 00cf | 0
11 | 00cf | 0

## Slide 14: 示例：三个数排序
R0
R1
R2
cf
“-”
ALU
CU
clk
rst
cf
s0~2
e0~2
done
CMP01
EXG01
CMP12
EXG12
CMP01S
EXG01S
HLT
done
s0, s1
s2, e1, e2
e0, e1
rst
思考题：如何优化？
cf
!cf
cf
!cf
cf
!cf
0
1
s1
0
1
s0
0
1
s2
e0, e1
Notes: 4个数的排序呢？

## Slide 15: 示例：三个数排序 (续)
R0
R1
R2
cf
“-”
ALU
0
1
s0
x0
x1
x2
x1
x0
SRT
x2
rst
done
4
clk
4
y1
y0
y2
CX01
CX12
CX01S
LOAD
rst
0
1
s1
0
1
s3
0
1
s2
HLT
s0~3 | e0~2 | done
x011 | 111 | 0
010x | cf,cf,0 | 0
1x00 | 0,!cf,!cf | 0
010x | cf,cf,0 | 0
xxxx | 000 | 1
y0
y1
y2
思考题：有符号数排序？
CU
clk
rst
cf
s0~3
done
e0~2

## Slide 16: 示例：时序乘法器
X，Y：输入数据，被乘数和乘数，4位无符号二进制数
Z：输出数据，8位积
Start：控制输入，启动乘法运算，高电平有效
Reset：控制输入，复位，高电平有效
Done：状态输出，运算结束指示，高电平有效
Clk：时钟输入
Start
Reset
4位乘法器
4
Y
4
X
8
Z
Done
Clk

## Slide 17: 乘法运算过程
X2
X3
X0
X1
Y2
Y3
Y0
Y1
×
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
Z2
Z3
Z0
Z1
Z6
Z7
Z4
Z5
+
(当Yi =1)
? ? ? ? =
X3X2X1X0
(当Yi =0)
0 0 0 0
D
B
A B
手工运算过程
+
0 0 0 0 0
Y3Y2Y1Y0
? ? ? ?
0 ? ? ? Z0
0 ? ? ?
Z0Y3Y2Y1
+
? ? ? ?
? ? ? ? Z1
? ? ? ?
Z1Z0Y3Y2
+
? ? ? ?
? ? ? ? Z2
? ? ? ?
Z2Z1Z0Y3
+
? ? ? ?
Z7 Z6Z5Z4Z3
Z3Z2Z1Z0
Z7Z6Z5Z4
C=0,A=0,D=X,B=Y
{C, A}=A+D*Y0
{A, B}={C,A,B}>>1
B
A
操作说明
C
{C, A}=A+D*Y1
{A, B}={C,A,B}>>1
{C, A}=A+D*Y2
{A, B}={C,A,B}>>1
{C, A}=A+D*Y3
{A, B}={C,A,B}>>1
迭代运算过程
Z = X × Y

## Slide 18: 乘法器结构
Clk
数据通路
控制单元
Start
4
Y
4
X
Done
8
Z
Init, Add,
Cnt, Shift
E, B0
Reset
Start
Reset
4位乘法器
4
Y
4
X
8
Z
Done
Clk

## Slide 19: 乘法器结构(续)
数据通路
Init: DX, BY, T0,
A0, C0
Cnt: TT-1
Add: {C, A}A+D
Shr: {C, A, B}{C, A, B}>>1
Start
Reset
Clk
控制单元
Init
Add
E
B0
Cnt
Shr
Done
2
被乘数
加法器
乘数
部分积
进位
4
4
4
B
A
C
D
4
4
4
X
Y
4
Z
计数器
T
检测0
E
0
Notes: 数据通路就是数据在被处理的过程中依次经过各种器件的次序和方向。

## Slide 20: 乘法器控制单元
状态图
S0
Done
Start/Init
Reset
S1
Cnt
S2
Shr
B0/Add
!B0
!Start
E
!E
Start
Reset
Clk
控制单元
Init
Add
E
B0
Cnt
Shr
Done
Init: DX, BY, T0,
A0, C0
Cnt: TT-1
Add: {C, A}A+D
Shr: {C, A, B}{C, A, B}>>1
思考题：Moore型如何？

## Slide 21: 乘法器控制单元(续1)
状态表
Reset
Start
B0
E
Sn
Sn+1
Done
Init
Add
Shr
Cnt
1
x
x
x
x
S0
0
0
0
0
1
0
0
x
x
S0
0
0
0
0
1
S0
0
1
x
x
S1
1
0
0
0
1
S0
0
x
0
x
0
0
0
1
0
0
x
1
x
S2
0
1
0
1
0
S1
S2
S1
0
x
x
0
0
0
1
0
0
0
x
x
1
S0
0
0
1
0
0
S2
S1
S2
Done = S0
Init = Start·S0
Add = B0 ·S1
Shr = S2
Cnt = S1

## Slide 22: Verilog描述乘法器
module multiplier(
input clk, resetn, start,
input [3:0] x, y,
output [7:0] z,
output done
);
reg [3:0] a, b, d;
reg c;
reg [1:0] state, next_state, t;
localparam S0=2’b00, S1=2’b01, S2=2’b10;
wire e;
assign e = ~|t;
assign z = {a, b};
Clk
Start
Reset
乘法器
4
Y
4
X
8
Z
Done

## Slide 23: Verilog描述乘法器(续1)
//state register
always @(posedge clk, posedge reset)
begin
if (reset) state <= S0;
else state <= next_state;
end
assign done = (state == S0);
//next state function
always @(*) begin
case (state)
S0: if(start) next_state = S1;
else next_state = S0;
S1: next_state = S2;
S0
Done
Start/Init
Reset
S1
Cnt
S2
Shr
B0/Add
!B0
!Start
F
!F

## Slide 24: Verilog描述乘法器(续2)
S2: if (!e) next_state = S1;
else next_state = S0;
default next_state = S0;
endcase
end
//datapath function
always @(posedge clk)
begin
case (state)
S0: if (start) begin
d <= x; b <= y;
a <= 4’d0; c <= 1’b0; t <= 2’b0;
end
S0
Done
Start/Init
Reset
S1
Cnt
S2
Shr
B0/Add
!B0
!Start
E
!E

## Slide 25: Verilog描述乘法器(续3)
S1: begin
t <= t - 2’b01;
if (b[0]) {c, a} <= a + d;
end
S2: begin
a <= {c, a[3:1]};
b <= {a[0], b[3:1]};
c <= 1’b0;
end
endcase
end
endmodule
S0
Done
Start/Init
Reset
S1
Cnt
S2
Shr
B0/Add
!B0
!Start
E
!E

## Slide 26: 乘法器仿真波形

## Slide 27: The End